## Slide 1: Remote DC Motor Monitoring and Controlling System
18M38127 LANG, Chen
18M38185 ZHANG, Zhiyang
18M38110 GAO, Tianyang

## Slide 2: Responsibility
LANG, Chen:
Hardware Design, Motor Controller Software
Zhang, Ziyang:
UI Design, Remote Controller Software
Gao, Tianyang:
UI Design, Remote Controller Software

## Slide 3: Functionality
Notes: 1. Control the output power and switch the operating direction of a DC motor; 2. Make the DC motor accelerate and decelerate when output power or operating direction is changed; 3. Collect the operating status of the entire system: voltage, current, temperature, motor direction and output power; 4. Prevent the entire system from overcurrent, overvoltage or undervoltage: 8~13V, 2A; 5. Control and monitor the entire system remotely via WIFI.

## Slide 4: Design
Hardware - Peripheral Circuits
Software - Motor Controller
Software - Remote Controller

## Slide 5: Hardware
Notes: 0. Explain the purposes of pins.
1. Why switching diode? (Protecting purpose, since the relay. Why relay? Because we want to cut off the power once...)

## Slide 6: Measure Voltage and Current
Input voltage is higher than 3.3V
ADC only measure voltage -> Use ohm’s law

## Slide 7: Why use capacitor?
Output signal from M5Stack GPIO pins are not stable sometimes)

## Slide 8: Control The Relay
Output power of the M5Stack GPIO pins is really low. Even though this relay can be driven with really small power.

## Slide 9: Software - Motor Controller
4 Tasks: Motor Drive, Status Scan, I2C Reader, Network
Priority: 4, 3, 2, 1
Period: 1ms, 50ms, 100ms, 10ms
- PWM Controlling needs output controlling signal with precise time interval. In our system, the frequency of the PWM wave is 100Hz.
Notes: The left one has the higher priority and shorter period.
Explain a little bit about I2C (transmission requires time) and Network (TCP connection)

## Slide 10: Software - Motor Controller
4 Tasks: Motor Drive, Status Scan, I2C Reader, Network
Priority: 4, 3, 2, 1
Period: 1ms, 50ms, 100ms, 10ms
- Scanning voltage and current is used to protect the entire system, so it must be done within a fixed period.
Notes: The left one has the higher priority and shorter period.
Explain a little bit about I2C (transmission requires time) and Network (TCP connection)

## Slide 11: Software - Motor Controller
Inter-Task Communication is done by MessageQueue.
xQueueCreate(), xQueueSend(), xQueueReceive()
Non-blocking message sending and receiving.
uxQueueSpacesAvailable()
Also means: No locks are used in the time-sensitive tasks.
- Cannot block the execution of the time-sensitive task, such as sending motor status while generating PWM waves.
Notes: Explain how to realize “non-blocking” sending and receiving.

## Slide 12: Software - Remote Controller
2 Tasks: Display, Network
Priority: 2, 1
Period: 25ms, 10ms
UI Design
  Status
  Command Menu
  Solve Flicker Issue

## Slide 13: User Interface
UI components
  Button panels
  Listbox
  Radiobox
Button functionalities
  Change screen
  Next/ Increment variable
  OK

## Slide 14: Demo
Monitoring Status (Screen 1)
Remotely Control (Screen 2)
Forward + Set Power
Backward
Stop
Set Power
Set Relay
Circuite Protection

## Slide 15: Any Questions?

## Slide 16: Thank you!